## Slide 1: CS / EE 320 Computer Organization and Assembly Language Spring 2024 Lecture 17
Shahid Masud
Topics: From Single Cycle MIPS to Multicyle MIPS, Pipelining

## Slide 2: Topics
Timing calculations in Single-Cycle Simple MIPS CPU
How to add pipelining in simple MIPS CPU
Detailed analysis of 5-Stage Pipelined MIPS CPU
Calculations Throughput, Latency, Critical Path of 5-Stage MIPS CPU
Design of individual Pipelined stages in a 5-Stage MIPS CPU
Hazards in Pipelined MIPS CIPS
  Structural Hazard (Hardware Related)
  Data Hazard (Due to Assembly program)
  Control Hazard (Architecture related)

## Slide 3: SIMPLE MIPS WITH NO PIPELINE

## Slide 4: Full Datapath – for practice of connections

## Slide 5: Full Datapath

## Slide 6: MIPS Datapath With Control

## Slide 7: BASICS OF PIPELINING

## Slide 8: What Is Pipelining
Laundry Example
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, and fold
Washer takes 30 minutes
Dryer takes 40 minutes
“Folding” takes 20 minutes
One load takes 90 minutes
A
B
C
D

## Slide 9: What Is Pipelining
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time

## Slide 10: Pipelining Lessons
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduces speedup
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20
Overlapping different operations

## Slide 11: Introducing Pipelining for MIPS

## Slide 12: Single-cycle MIPS RISC Architecture
Example: simple MIPS architecture
Critical path includes all of the processing steps
Write Back
Inst. Fetch
Inst. Decode
Execute
Memory
Inst.
Memory
Register File
ALU
Data Memory
PC
Controller

## Slide 13: Execution on Single-cycle MIPS Architecture
Time
Example program
CT=6ns; CPU Time = 5 x 1 x 6ns = 30ns
AND R1,R2,R3
How to improve?
XOR R4,R2,R3
SUB R5,R1,R4 ADD R6,R1,R4 MUL R7,R5,R6
CPU Time = IC x CPI x CT

## Slide 15: Re-Using Idle Resources
Write Back
Inst. Fetch
Inst. Decode
Execute
Memory
Inst.
Memory
Register File
ALU
Data Memory
PC
Controller
Each processing step finishes in a fraction of a cycle
Idle resources can be reused for processing next instruction

## Slide 16: Non Pipeline Architecture
Time
CPU Time = IC x CPI x CT
Example program
CT=1.5ns; CPU Time = 5 x 5 x 1.5ns = 37.5ns > 30ns
WORSE!!
AND R1,R2,R3
XOR R4,R2,R3
SUB R5,R1,R4 ADD R6,R1,R4 MUL R7,R5,R6

## Slide 17: Developing a Multi‐cycle Data Path
5

## Slide 18
Write Back
Inst. Fetch
Inst. Decode
Execute
Memory
Inst.
Memory
Register File
ALU
Data Memory
PC
Controller
Develop Simple Five Stage MIPS Pipeline
A pipelined load-store architecture that processes up to one instruction per cycle

## Slide 19: Identify Distinct Processing Stages in Architecture
Five stage pipeline
Critical path determines the cycle time
Write Back
Inst. Fetch
Inst. Decode
Execute
Memory
Inst.
Memory
Register File
ALU
Data Memory
PC
1.5ns
1.5ns
1.25ns
1.05ns
0.7ns

## Slide 20: Identify CPU Operations where Pipeline Registers could be Inserted

## Slide 21: Recap - Full Datapath

## Slide 22: Instruction Fetch
D Read an instruction from memory (I-Memory)
Use the program counter (PC) to index into the I- Memory
Compute New PC (NPC) by incrementing current PC
What about branches?
  (later?)
D Update pipeline registers
Write the instruction into the pipeline registers

## Slide 23: Instruction Fetch
Memory
PC
+
4
NPC
Instruction
Pipeline Register
Why increment by 4?
NPC = PC + 4
clock
clock
Branch Target

## Slide 24: Instruction Decode
D Generate control signals for the opcode bits
D Read source operands from the register file (RF)
Use the specifiers for indexing RF
How many read ports are required?
D Update pipeline registers
Send the operand and immediate values to next stage
Pass control signals and NPC to next stage

## Slide 25: Instruction Decode
Register File
ctrl
Pipeline Register
NPC
NPC
Instruction
Pipeline Register
reg
reg
decode
target

## Slide 26: Execute Stage
D Perform ALU operation
Compute the result of ALU
Operation type: control signals
First operand: contents of a register
Second operand: either a register or the immediate value
Compute branch target
Target = NPC + immediate
D Update pipeline registers
Control signals, branch target, ALU results, and destination

## Slide 27: Execute Stage
ALU
ctrl
Pipeline Register
NPC
Target
Pipeline Register
reg
reg
+
reg
ctrl
Res

## Slide 28: Memory Access
Access data memory
Load/store address: ALU outcome
Control signals determine read or write access
Update pipeline registers
ALU results from execute
Loaded data from D-Memory
Destination register

## Slide 29: Memory Access
ctrl
Pipeline Register
Target
Pipeline Register
Res
reg
Dat
ctrl
Res
Memory
addr
data
data

## Slide 30: Register Write Back
Update register file
Control signals determine if a register write is needed
Only one write port is required
Write the ALU result to the destination register, or
Write the loaded data into the register file

## Slide 31
Improving Resource Utilization

## Slide 32: Improving CPU Resource Utilization
Efficient MIPS CPU Design
Can we eliminate two adders?
How to share (or reuse) a resource (say ALU) in different clock cycles?
Store results in registers.
Of course, more multiplexing may be required!
Resources in this design: RF, ALU, MEM.

## Slide 33: Single Cycle Datapath
1
0
s2
ins[25‐0]
ja[31‐0]
28
0
+
+
s2
1
4
PC+4[31‐28]
ins[25‐21]
1
0
PC
IM
ad
ins
rad1 rad2 wad
wd
rd1 rd2
RF
ad
rd
ALU
ins[20‐16]
0
ins[15‐11]
1
0
1
DM
wd
sx
ins[15‐0]
16

## Slide 34: Merge IM and DM, Rearrange Diagram
0
0
s2
ins[25‐0]
ja[31‐0]
28
1
+
+
s2
1
4
PC+4[31‐28]
ins[25‐21]
0
PC
rad1 rad2 wad wd
rd1 rd2
RF
ALU
ins[20‐16]
0
ins[15‐11]
1
ad
rd
Mem
wd
1
sx
16
ins[15‐0]

## Slide 35: Combine Adders - Rearrange Diagram
1
0
s2
ins[25‐0]
ja[31‐0]
28
0
1
PC+4[31‐28]
ins[25‐21]
0
PC
rad1 rad2
wad
wd RF
rd1
rd2
ALU
ins[20‐16]
0
ins[15‐11]
1
ad
rd
Mem
wd
4
1
sx
16
ins[15‐0]
s2

## Slide 36: Introduce registers
1
0
s2
ins[25‐0]
ja[31‐0]
28
0
1
PC+4[31‐28]
ins[25‐21]
A
0
PC
rad1 rad2
wad
wd RF
rd1
rd2
ALU
ins[20‐16]
0
ins[15‐11]
1
ad
rd
Mem
wd
4
IR
B
1
sx
16
s2
DR ins[15‐0]
RES

## Slide 37: Introduce ALU multiplexers at Input and Output
s2
ins[25‐0]
28
ja[31‐0]
PC+4[31‐28]
ins[25‐21]
A
2
0
PC
rad1
rad2
wad
wd RF
rd1
rd2
ALU
ins[20‐16]
0
ins[15‐11]
1
ad
rd
Mem
wd
4
IR
B
1
0
1
0
1
sx
16
s2
RES
DR ins[15‐0]

## Slide 38: Final: Efficient Multi‐Cycle Data Path
ins[25‐0]
ja[31‐0]
28
rad1
s2
ins[25‐21]
IR
A
2
PC[31‐28]
0
0
1
PC
RF
rad2
wad wd
rd1
rd2
ALU
ins[20‐16]
ins[15‐11]
ad
rd
Mem
wd
Res
1
0
1
0
4
B
0
1
sx
16
s2
ins[15‐0]
DR
1
2
3
1
0
Mux at Memory Input
Mux at Register File Input
One memory for lw / sw
One ALU for EXE and Address Calculation
Several MUXes introduced

## Slide 39: MIPS Pipelined Datapath
WB
MEM
Right-to-left flow leads to hazards

## Slide 40: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 41: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle
    Highlight resources used
  c.f. “multi-clock-cycle” diagram
    Graph of operation over time
We’ll look at “single-clock-cycle” diagrams for load & store

## Slide 42: RF is two operations in One Clock Cycle
Assume Write is when clock is going up
Assume Read is when Clock is going down
(you can assume otherwise too, but two operations in one clock cycle)
Read on this
Edge
Write on this
Edge
Clock Edges

## Slide 43: IF for Load, Store, …

## Slide 44: ID for Load, Store, …

## Slide 45: EX for Load

## Slide 46: MEM for Load

## Slide 47: WB for Load
Register
Write

## Slide 48: EX for Store

## Slide 49: MEM for Store

## Slide 50: WB for Store

## Slide 53: The Basic Pipeline For MIPS – Simplified Diagram
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
I
n
s
t
r.
O
r
d
e
r

## Slide 54: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 55: Multi-Cycle Pipeline Diagram
Form showing resource usage for different instructions

## Slide 56: Single-Cycle Pipelined Diagram
State of pipeline in a given cycle

## Slide 57
Pipeline Performance Estimation

## Slide 58: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
Four loads:
  Speedup = 8/3.5 = 2.3

## Slide 59: Pipelined Architecture
D Example program
CT=1.5ns; CPU Time = 9 x 1 x 1.5ns = 13.5ns
AND R1,R2,R3
XOR R4,R2,R3
SUB R5,R1,R4 ADD R6,R1,R4 MUL R7,R5,R6
Time
CPU Time = IC x CPI x CT
What is the cost of pipelining?

## Slide 60: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 61: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 62: Multi‐cycle Control Path
24

## Slide 63: Multi‐cycle Control Design
Break instructions into cycles
Put cycle sequences together
Control signal groups and micro operations
Control states and signal values
Control state transitions

## Slide 64: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation

## Slide 65: Pipelined Control with Connections

## Slide 66: Readings
Chap 4 of P&H Textbook